## Slide 1: System noise temperature and G/T ratio
By
S.Sadhish Prabhu

## Slide 2: Noise temperature
It provides a way for determining how much thermal noise is generated by active and passive devices in the receiving system.
- At same physical temperature at the input of the amplifier
All objects with physical temperature , Tp greater than 0o K generate electrical noise at the receiver in microwave frequencies.

## Slide 3: Noise power
Pn = k Tp Bn - (1.1)
K = Boltzman’s constant
(1.38X10-23 J/K = -228.6dBW/K/Hz)
Tp = Physical temperature of source in kelvin degree
Bn = Noise bandwidth in which the noise power is measured in hertz
Pn = avaliable noise power
k Tp = noise power spectral denisty in watts per hertz
It is constant upto 300GHz

## Slide 4: Method for designing receiving system #1
Set the BW in the receiver large to allow the signals keeiping the noise power as low as possible
Equ (1.1) can be the equivalent noise band width unfortunately this cant be determined in the receiver
So, 3-dB is chosen in the receiver

## Slide 5: Method for designing receiving system #2
Keep the noise temperature low
Immerse the front end amplifier in liquid helium to hold the temperature at 4 degree Kelvin
Expensive and difficult to maintain
Use GaAsFET amplifiers with noise temperature of 70K at 4 GHz and 180 K at 11 GHz without cooling

## Slide 6: Performance of the receiving system
Find the thermal noise against which the signal must be demodulated
To do this system noise temperature must be found out , Ts
Ts - noise temperature of a source ,
located at the input of a noise less receiver,
which gives the same noise power as the original receiver, measure at the output of the receiver

## Slide 7: Noise power
Noise power at the input of demodulator is,
Pno = k Ts Bn Grx watts - (1.2)
Where
Grx = gain of the receiver from RF input to the demodulator input

## Slide 8: Problem 1
An antenna has noise temperature of 35 K and is matched into a receiver which has a noise temperature of 100 K calculate:
a) noise power density and
b) the noise power for a bandwidth of 36 MHz.

## Slide 9: Solution
a) NO = k TN = 11.38 x 10-23x (35 + 100) = 1.86 x 10-21 J
b) PN = NO BN = 1.86 x 10-21x 36 x 106 = 0.067 pW

## Slide 10: Carrier-to-noise ratio
Let the antenna deliver a power Pr to the receiver RF input
The signal power at the demodulator input is Pr Grx watts
Carrier –to-noise ratio at the demodulator is,

## Slide 11: Calculation of system noise temperature
LNA
BPF
Mixer
IF amp
Local oscillator
BPF
Antenna
Pr
Gm
GIF
IF output
Grf
Single Super heterodyne receiver

## Slide 12: Noise model of receiver
+
+
+
Gain
Grf
Gain
Gm
Gain
Gif
Trf
Tm
Tif
Tin
Pn
Noiseless RF Amplifier
Noiseless mixer
Noiseless IF Amplifier
a) The Noisy amplifier and down converters are replaced by noise less units with equivalent noise generators at their inputs

## Slide 13: Noise model of receiver
+
Gain
Grf.Gm.Gif
Ts
Tin
Noiseless Rreceiver
+
Gain
Gl
Tno
Noiseless lossy device
Pn
Tin
Pn
b) All noisy unit replaced with one noiseless amplifier with a single noise source Ts
c) The lossy device is replaced with lossless device , with a signal noise source Tno

## Slide 14: Noise power
Total noise power :
Pn= GIF k TIF Bn + GIFGmkTmBn + GIFGmGRFkBn(TRF+Tin )
Pn= GIFGmGRF [(k TIF Bn )/GRFGm +( kTmBn)/GRF +(TRF+Tin) ]
= GIFGmGRF k Bn [TRF+Tin +Tm /GRF+ TIF /(GRFGm ) ]
Here Ts generates the same noise power Pn at its output if
Pn = GIFGmGRF k Ts Bn
Noise power in the noise model (b) will be equal to (a) if
k Ts Bn = k Bn [TRF+Tin +Tm /GRF+ TIF /(GRFGm ) ]
Hence,
Ts = [TRF+Tin +Tm /GRF+ TIF /(GRFGm ) ]
Conclusion:
The receiver gives less noise as the gain from each stage is added hence the noise contributed by the IF amplifier and later sages can be ignored

## Slide 15: Calculation of system noise temperature
LNA
BPF
Mixer
BPF
First
IF amplifier
First L.O.
Second L.O.
Mixer
BPF
Baseband out put
Demodulator
BPF
Second
IF amplifier
D
900 to 1400 MHz
Double Super heterodyne receiver

## Slide 16: G/T ratio for earth station
2
2
Figure of merit Gives the quality of an earth station
The link equation can be rewritten as :
Constants

## Slide 17: Antenna Noise Temperature
Noise Temperature of an Antenna as a Function of Elevation Angle:

## Slide 18: Problem 2
Suppose we have a 4 GHz receiver with the following gains and noise temperature
Tin = 50 K
Trf = 50 K
Tin = 500 K
Tif = 1000 K
Grf = 23 dB
Gm = 0 dB
Gif = 30 db
Calculate the system noise temperature.

## Slide 19: Solution
Ts = 152.5 K

## Slide 20: Problem 3
An earth station antenna has a diameter of 30 m , has an overall efficiency of 68% , and is used to receive a signal at 4150 MHz. At this frequency , the system noise temperature is 79 K when the antenna points at the satellite at an elevation angle of 28 degree. What is the earth station G/T under these conditions? If heavy rain causes the sky temperature to increase so that the system noise temperature rises to 88 K , what is the new G/T value

## Slide 21: Solution
G/T = 41.6 dBK-1
If heavy rain
G/T = 41.2 dBK-1